## Slide 1: Analysis of Security Certificates
Team Supercalifragilisticexpialidocious
Anh Minh Tran
Ankur Lohchab
Tomáš Madeja

## Slide 2: Certificates
Thinklogical TLX1280
genuscreen 7.0
2
FM1280 V05
3
1
genuscreen 7.0
2
FM1280 V05

## Slide 3: Thinklogical TLX1280 Matrix Switch
EAL 4
Optic fiber switch that uses multimode fiber optics.
Transmit and receive a digital video pulse stream without alteration or interpretation of the original signal.
Embedded keyboard, mouse, USE 1.1, USB 2.0 (high speed up to 480 Mbps), and audio signals are also transmitted.
1280 x 1280 routing system, 40 Data Input and Output Cards (32 optical input and output ports each).
Data Input and Output Cards to connect with single or multiple ports.

## Slide 4: Thinklogical TLX1280 Matrix Switch
Security Functional Components
Security Functional Requirements | 
FDP_ETC.1 | Export of user data without security attributes
FDP_IFC.1 | Subset information flow control
FDP_IFF.1 | Simple security attributes
FDP_ITC.1 | Import of user data without attributes
Security functional requirements are similar to the PSSPP

## Slide 5: Thinklogical TLX1280 Matrix Switch
Security Objective Environment | 
OE.EMISSION | Limited electromagnetic radiation
OE.MANAGE | Install and manage as per directions
OE.NOEVIL | Authorised user non hostile
OE.PHYSICAL | Physical security of devices
OE.SCENARIO | Attached device vulnerability not TOE concern
Security Objectives
Security Objective | 
O.CONF | No access of info
O.CONNECT | No sharing of information

## Slide 6: Thinklogical TLX1280 Matrix Switch
Threat | Definition
T.INSTALL | The TOE may be delivered and installed in a manner which violates the security policy.
T.ATTACK | An attack on the TOE may violate the security policy
T.RESIDUAL | Residual data may be transferred between different port groups in violation of data separation security policy.
T.STATE | State information may be transferred to a port group other than the intended one.
Attacker Model

## Slide 7: Thinklogical TLX1280 Matrix Switch
Testing | 
Developer Test followed by Evaluator Test | No details of the type of test and methodology
Evaluators tested sample of Developer tests | Evaluator asses that developer have performed test correctly
Testing & Evaluation

## Slide 8: Thinklogical TLX1280 Matrix Switch
Attacker model details are missing.
No details of evaluation procedure.
Test performed too generic, details missing.
Review

## Slide 9: Certificates
Thinklogical TLX1280
genuscreen 7.0
2
FM1280 V05
3
1
genuscreen 7.0
2
FM1280 V05

## Slide 10: genuscreen 7.0
Main functions:
monitoring data traffic
protecting LAN/Internet interface (firewall)
enabling the exchange of encrypted data (VPN)
Optional SIP relay functionality consists only of the software (on CD or USB) and its documentation checksum of software on CD/USB provided cryptographic algorithms are part of TOE, e.g. RNG
EAL 4+
Evaluated by developer and an independent evaluator
test procedures = scripts in Ruby, Perl or Shell
Developer: local and live tests
Independent eval.: only live tests but with additional vulnerability tests
Details on the tests are not provided

## Slide 11: genuscreen 7.0
Security Assurance Rationale:
  ALC_FLR.2 Flaw reporting procedures
  ASE_TSS.2 TOE summary specification with architectural design summary
  AVA_VAN.4 Methodical vulnerability analysis
TOE Scurity Functionality | 
SF_PF | Packet Filter
SF_NS | Network Separation
SF_IPSEC | IPSec Filtering
SF_SIP | SIP Relay
SF_IA | Identification and Authentication
SF_AU | Audit
SF_SSH | SSH Channel
SF_ADM | Administration
SF_GEN | General Management Facilities
Security Functional Components

## Slide 12: genuscreen 7.0
Security Objectives
Security Objectives | 
O.AUTH | The TOE must assure that only administrators can change the packet filter, VPN and SSH configuration.
O.MEDIAT | The TOE must mediate the flow of all data between all connected networks.
O.CONFID | The TOE must assure that data transferred between the networks protected by firewall components is kept confidential unless explicitly configured otherwise.
O.INTEG | The TOE must assure that data transferred between the networks protected by firewall components cannot be modified unnoticed unless explicitly configured otherwise.
O.NOREPLAY | The TOE must assure that data transferred between the networks behind the firewall components cannot be reinjected at a later time unless explicitly configured otherwise.
O.AUDREC | The TOE must provide an audit trail of security-related events, and a means to present a readable and searchable view to administrators, service users and revisors.
O.AVAIL | The TOE must optionally provide a fail over solution where the services of a failing system are taken over by a peer machine.

## Slide 13: genuscreen 7.0
Threats
Threats | 
T.NOATUH | Anonymous user enters a system without athentication
T.SNIFF | An anonymous user might gain access to the sensitive data passing between the protected networks. Attack method is packet inspection of Internet traffic.
T.SELPRO | An anonymous user might gain access to the TOE and read, modify or destroy security sensitive data on the TOE, by sending IP packets to the TOE and exploiting a weakness of the protocol used.
T.MEDIAT | An anonymous user might send non-permissible data that result in gaining access to resources which is not allowed by the policy. The attack method is construction of IP packets to circumvent filters.
T.MSNIFF | An anonymous user might gain access to the configuration or audit data passing between the management system and a firewall component. Attack method is packet inspection of Internet traffic.
T.MODIFY | An anonymous user might modify the sensitive data passing between the protected networks. Attack method is packet interception and modification of Internet traffic.
T.MMODIFY | An anonymous user might modify the configuration or audit data passing between the management system and a firewall component. Attack method is packet interception and modification of Internet traffic.

## Slide 14: genuscreen 7.0
Assumptions
Assumptions | 
A.PHYSEC | The management system and the firewall components of the TOE are physically secure. Only administrators have physical access to the TOE. This must hold for the management system and the firewall components.
A.INIT | The TOE was initialised according to the procedure described in the docu-mentation.
A.NOEVIL | Administrators, service users and revisors are non-hostile and follow all administrator guidance; however, they are capable of error. They use passwords that are not easily guessable.
A.SINGEN | Information can not flow between the internal and external network, unless it passes through the TOE.
A.TIMESTMP | The environment provides reliable timestamps.
A.ADMIN | Administrators, service users and revisors using the administrative GUI on the management system or the firewall components work in a trusted network directly connected to the system.
A.HANET | The environment provides a physical separate network for TSF data transfer for the optional high availability setup.
A..REMOTE_AUTH | The server for external LDAP authentication of genucenter administrators and revisors is located in a secure network.

## Slide 15: Certificates
Thinklogical TLX1280
genuscreen 7.0
2
FM1280 V05
3
1
genuscreen 7.0
2
FM1280 V05

## Slide 16: FM1280 V05
Memory
OTP EEPROM
EEPROM
ROM
System RAM
Coprocessor RAM
PAE RAM
CLA RAM
Interface
ISO/IEC 14443 Type A contactless
ISO/IEC 7816 contact
GPIO
SPI
High Speed SPI
I2C
UART
Physical protection
Watch Dog Timer
Security Controller
Environment Detection Circuits
Light Sensor
Clock Frequency Monitor
Temperature Sensor
Voltage Sensor
Glitch Sensor
Active Shielding

## Slide 17: FM1280 V05
Algorithm
RNG
DES/TDES
AES
RSA
ECC
Coprocessors
TRNG
CRC-CCITT
DES/TDES
AES
PAE for RSA
PAE for ECC
HASH (SHA1/SHA256)
Chinese Domestic Algorithm

## Slide 18: FM1280 V05
Threats | 
T.Leak-Inherent | Inherent information leakage
T.Phys-Probing | Physical probing
T.Malfunction | Malfunction due to enviromental stress
T.Phys-Manipulation | Pysical manipulation
T.Leak-Forced | Forced information leakage
T.Abuse-Func | Abuse of functionality
T.RND | Deficiency of random numbers
Security Objectives | 
O.RSA | Encryption, decryption
O.ECC | Signature generation and verification, DH, point multiplication and addition
O.TDES | Encryption, decryption
O.AES | Encryption, decryption
Attacker/Threat Model

## Slide 19: FM1280 V05
Developer Tests
Engineering samples
Wafers
Simulation tool
Vulnerablity Analysis
Deign and Implementation review
Code review of crypto lib
Code review of boot code
Validation tests of features
Review based on “JIL Attack Methods for Smartcards and Similar Devices”
Penetration tests
Testing & Evaluation
Evaluator Tests
SFI
SFI interfaces
Security mechanisms
Developer tests
Augmented developer tests

## Slide 20: Thank You